## Slide 1: Hamming Code
By: Htoo Thein & Shannon Sremac

## Slide 2: What is Hamming Code?
Linear error correcting code
(7,4) Hamming was developed by Richard W. Hamming in 1950
Hamming Code is used to check for bit error in data transmission
There are 4 parity bits that will check specific bits
Each parity bit has their own unique set of bits to check
A byte (8 bits) will have 4 parity bits added to the data

## Slide 3: How to Implement Hamming Code
Take a byte of data
Add parity bits at positions 1, 2, 4 and 8
The parity bit at position 1 will check bits 1,3,5,7,9,11
The parity bit at position 2 will check bits 2,3,6,7,10,11
The parity bit at position 4 will check bits 4,5,6,7,12
The parity bit at position 8 will check bits 8,9,10,11,12
A parity bit will be 0 if even number of 1’s is checked, 1 if odd.

## Slide 4: Example byte: 11110000
Add 4 parity bits at bit location 1, 2, 4, and 8
  _ _ 1 _ 1 1 1 _ 0 0 0 0
For parity bit 1, count the number of 1’s in location 1, 3, 5, 7, 9, 11
  x _ 1 _ 1 1 1 _ 0 0 0 0
  3 1’s counted so parity bit 1 = 1
  1 _ 1 _ 1 1 1 _ 0 0 0 0
For party bit 2, count the number of 1’s in location 2,3,6,7,10,11
  1 x 1 _ 1 1 1 _ 0 0 0 0
  3 1’s counted so parity bit 2 = 1
  1 1 1 _ 1 1 1 _ 0 0 0 0
For parity bit 4, check position 4, 5, 6, 7, 12
  1 1 1 x 1 1 1 _ 0 0 0 0
  3 1’s counted so parity bit 4 = 1
  1 1 1 1 1 1 1 _ 0 0 0 0
For parity bit 8, check position 8, 9, 10, 11, 12
  1 1 1 1 1 1 1 x 0 0 0 0
  0 1’s counted, 0 is considered even so parity bit 8 = 0
  1 1 1 1 1 1 1 0 0 0 0 0

## Slide 5: Checking and correcting error
Example: sender 1 1 1 1 1 1 1 0 0 0 0 0, receiver: 1 1 1 1 1 1 0 0 0 0 0 0
Bit 7 is the bad bit!
Check all parity bits
Bit 1 claims odd number of 1’s in position 3, 5, 7, 9, and 11
  1 1 1 1 1 1 0 0 0 0 0 0
  Bit 1 is wrong
Bit 2 claims odd number of 1’s in position 3, 6, 7, 10 and 11
  1 1 1 1 1 1 0 0 0 0 0 0
  Bit 2 is wrong
Bit 4 claims odd number of 1’s in position 5, 6, 7, 8, and 12
  1 1 1 1 1 1 0 0 0 0 0 0
  Bit 4 is wrong
Bit 8 claims even number of 1’s in position 9, 10, 11 and 12
  1 1 1 1 1 1 0 0 0 0 0 0
  Bit 8 is correct!
Therefore the bad bit is (1+2+4) = 7!
Corrected data: 1 1 1 1 1 1 1 0 0 0 0 0